## Slide 1
Celestial Day’s Work in Navigation
NN220-14
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation– Updated May 2023
SEANAV I United States Naval Academy

## Slide 2
References
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The American Practical Navigator, Pub. No. 9, Bowditch, VOL. 1, 2019 Edition -Surface Ship Navigation Department Organizations and Regulations Manual (NAVDORM), COMNAVSURFPAC/COMNAVAIRPAC/COMNAVAIRLANT/COMNAVSURFLANT INSTRUCTION 3530.4 series -Nautical Almanac

## Slide 3
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 – DESCRIBE The planning involved to conduct CELNAV. 2 - DEFINE Local Hour Angle in relation to identifying Celestial Bodies (CBs). 3 - DESCRIBE Dead Reckoning and relationship of Assumed Position (AP) to Time. 4 - EXPLAIN How to identify the best CBs to navigate from. 5 - EXPLAIN Circle of Equal Altitude. 6 - DESCRIBE The Altitude Intercept Method. 7 - DEFINE Sunrise / Sunset in relation to the Visible Horizon. 8 - DESCRIBE The importance of accurate Gyro Compasses and effect on Navigation / Weapon Systems. 9 - EXPLAIN How to calculate Gyro Error from the bearing of Sunrise / Sunset. 10 - DESCRIBE How to fix from the Sun using a Running Fix (Sun Run Sun). 11 - DESCRIBE Meridian Passage and the calculation of Latitude. 12 - DESCRIBE The Day’s Work in Celestial Navigation.

## Slide 4
What is the U.S. Navy Policy on CELNAV?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 5
What is the U.S. Navy Policy on CELNAV?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 6
What is the U.S. Navy Policy on CELNAV?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Per the NAVDORM, Celestial Navigation must be conducted, weather permitting, every day in Open Ocean.
-This means that CELNAV is being conducted around the world by ALL surface ships IAW NAVDORM.
-We must familiarize ourselves with the process, commonly called a Celestial’s Days Work in Navigation.

## Slide 7
Celestial Navigation
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-In the modern navigation era with GPS positioning, CELNAV is primarily used to verify the accuracy of GPS in Open Ocean and equipment accuracy.
-It also doubles as practical experience in sight reductions and celestial fix calculations for bridge watchstanders and Junior Officers.
-It provides an effective fallback should GPS fail or be denied while in Open Ocean transits.
-It is an essential skillset for a mariner.

## Slide 8
Celestial Navigation
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Many ships will conduct Trans-Oceanic voyages only by fixing celestial positions.
-Within sight of land, the ship will receive it’s last fix by GPS, Visual or RADAR means.
-From there, with an Assumed Position (AP) based on their Dead Reckoning (DR), they can conduct CELNAV and update their position with celestial fixes for the entirety of the transit!
-With the NAVDORM policy on Day’s Work in Navigation, we can lay the foundation for how to effectively determine our position using ONLY CELNAV.

## Slide 9
CELNAV Planning
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Effective CELNAV relies on planning.
-As we discussed previously, the Apparent Movement of Celestial Bodies (CBs) can mean their Geographic Positions (GPs) can move as much as 900kts across the surface of the Earth. That is 1.5nm per minute!
-Using the Horizon Coordinate System, the Altitude (angle between the CB and the visible horizon) and the Azimuth (true bearing from our position to the CB) will change as well.
-Time and our AP become critical factors.
-We need to calculate the time window of Twilight, as this is the time when we can see both our horizon and the best CBs needed for CELNAV.
-With thousands of CBs in the sky, we need the right ones. To do so, we predict its Altitude and Azimuth based on our AP.

## Slide 10
Assumed Position / Dead Reckoning
So how do we predict our position in the future?
On a paper chart, we draw a line based on our Course from our last fix, and measure distance based on speed to calculate time. This is Dead Reckoning (DR).
ECDIS systems, such as VMS, have a Route Monitoring function. This provides the User with Time information for future positions.
Using STELLA, we input an initial Fix as a Latitude and Longitude based on our charted position and the Time. We must input our Course and Speed to enable the software to calculate our position in the future and relate this to Celestial Information.

## Slide 11
Assumed Position vs Time
We can now predict our Assumed Position (AP) in the future. But remember, the time of day impacts which bodies we can use to navigate.
We can only see Celestial Bodies and the Visible Horizon after Sunset / before Sunrise during the period of Twilight. After this it becomes too dark to see the Visible Horizon.
After Sun Rise, we can see the Visible Horizon, the Sun and sometimes the Moon. We can therefore navigate from these objects.
The Nautical Almanac gives us the Time of Sunrise / Sunset / Civil and Nautical Twilight for every day of the year and every Latitude.

## Slide 12
Assumed Position vs Time
So using our AP’s Latitude (DR) we can calculate the Time of SR/SS/Twilight based on the Greenwich Meridian.
Alternatively, STELLA will also work out the Times and will take into account our AP(DR)!
However, using our AP, we must then account for our Longitude East or West.
Rather than doing the Math, the Nautical Almanac has a useful Arc to Time Table to help us out!
Remembering:
15° of Longitude = 1Hr of Time.
1° of Longitude = 4mins.
Provides Times associated with DR position

## Slide 13
Identifying Stars
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Now that we know the time of SR/SS and Twilight based on our AP, we can begin to identify the best stars to use.
-We will need a minimum of 3, since we need 3 LOPs for a fix.
-The Nautical Almanac list the 57 best stars to use for CELNAV.
-We will not be able to see all of them from our position, so we have to narrow down our focus.

## Slide 14
CELNAV Planning
We can predict the Declination and Greenwich Hour Angle (GHA) of any Celestial Body for a specific time using either the Nautical Almanac or STELLA. Remember that these are a CB’s coordinates on the Celestial Sphere!
As CBs rise, their Altitude in relation to Visible Horizon increases and then decreases, just as with the Sun.
We convert these coordinates to relate to us on the Earth surface in terms of Azimuth and Altitude. This is done via STELLA or calculations using Strip Forms.
Visible Horizon
Altitude of 40°
Altitude of 48°
Similarly, their Azimuth (True Bearing) also changes over time.
Bearing 004°
Bearing 352°
The further a Celestial Body is from the Celestial Pole, the higher its speed of relative motion and the more the Altitude and Azimuth will change over time.
Watch Video: https://www.youtube.com/watch?v=V97HQcbozeQ

## Slide 15
CELNAV Planning
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The Altitude of a CB changes with Latitude.
-At the North Pole, we see Polaris at an Altitude of 90°. If we move further south, the Altitude will decrease until we go below the Equator and Polaris is no longer visible.
-GHA is the equivalent of Longitude on the Celestial Sphere. The GHA of a CB can be expected to change at approx. 15° per hour, just like our time zones on Earth.
-GHA is used to help us find the Azimuth at which we will see a CB, which will be based on the Time and Longitude of our AP.
-The relationship between our Longitude and GHA is called the Local Hour Angle (LHA).

## Slide 16
Celestial Navigation Planning
0⁰
090⁰E
090⁰W
180⁰
AP(DR) Longitude 066⁰W
First Point of Aries GHA 192⁰
LHA
LHA is always measured westwards from Observer’s Longitude.
LHA is the difference between Longitude of the Observer at their AP and the GHA of a Celestial Body at a specific Time.
LHA = GHA – West Longitude or GHA + East Longitude.
Greenwich Mean Line
Rather than calculating our LHA in relation to each individual CB, LHA is normally based on the GHA of the First Point of Aries, as the reference point to the Stars.
Using LHA and Publication 249 Sight Reduction Tables, we can immediately identify the best Stars to navigate from.

## Slide 17
Identifying Stars
Using the Local Hour Angle (LHA) we can predict which Stars we will be able to see.
Publication 249 – The Sight Reduction Tables is broken down into 3 Volumes. Volume 1 lists the 57 best stars, as detailed in the Nautical Almanac.
Using our Latitude and the calculated LHA, we can enter the Publication and it will show us the 7 best stars based on our Assumed Position (AP), based on Magnitude (Brightness), Separation (at least 30° between CBs) and Altitude (between 20°-60°).
For each of the 7 stars it lists:
The Altitude or Height Calculated above the horizon.
The Azimuth or True Bearing we must look down.
It also highlights the best 3 stars for a fix.
Latitude
Local Hour Angle

## Slide 18
Identifying Stars
STELLA will also complete this function for us electronically.
Based on our AP (DR), it will list the best Celestial Bodies to fix off of and present them on a Sky Chart.
The 7 best stars to use are highlighted in Red and Yellow.
However, sometimes, cloud can obscure the sky so we can’t always see the best stars. STELLA will display the Altitude and Azimuth of all stars of the 57 best navigable.
But remember, this is a snap shot for a specific Time in space. These objects are constantly moving, so their Altitude and Azimuth might be a little different based on the time we take the Sight.
Time, Date and DR position (AP).
List of Celestial Bodies, including Planets.

## Slide 19
Using the Stars
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-So we have covered what we must do before we take sights:
Calculate our AP (DR) based on Initial Fix, Course, Speed and Time.
Calculate the Time of Sunrise/Sunset and Twilight based on our DR.
Identify which Celestial Bodies we are going to use, based on LHA, PUB 249 and/or STELLA. This will provide use with both the Altitude (Hc) and the Azimuth (Zn) of the best CBs from our AP.
Additionally, we must calibrate our Sextants, know our Height of Eye, Atmospheric Pressure and Temperature so that our Sight Reductions are accurate.
-We are almost ready to take sights!
-But first, let’s describe how we use the stars to create LOPs.

## Slide 20
Circle of Equal Altitude
By taking a Sight, we are measuring the Altitude (Angle) of a Celestial Body between the Visible Horizon (0°) and our Zenith above us (90°).
Using the Math:
90° - Altitude = CO-ALTITUDE.
CO-ALT x 60nm = Distance (NM)
This gives us a distance from the Celestial Body’s Geographical Position on the Earth’s Surface. Like a radar range, we use it as an LOP.
However, the Altitude from a single object only tells us that we are on a circle of distance. Our position could be anywhere on that circle.
This is called a Circle of Equal Altitude and it is why we need at least 3 x LOPs in order to accurately fix our position.

## Slide 21
Circle Of Equal Altitude
The Altitude of a Celestial Body is proportional to the Distance from it’s Geographic Position.
Star / Celestial Body
GP
30°
3,600NM
When we look up at 90°, our Zenith, if we see a Celestial Body above us we are at it’s Geographic Position.
As we move away from the GP, it’s Altitude in relation to us reduces.
90° – Altitude = COALT
90° - 30° = 60°
60° x 60nm = 3600nm
AP
(DR)
When the Celestial Body’s Altitude dips below 0°, it has gone from the Horizon to beneath the Visible Horizon. We can no longer see it.

## Slide 22
Using the Stars
Once we have identified our preferred Celestial Bodies, we can take a minimum of 3 Sights. Generally, we take more just in case we misidentify a Star.
GP1
GP2
GP3
… A 3-point visual fix

## Slide 23
Based on an earlier fix, we have used STELLA to predict our Assumed Position (Dead Reckon) to get the predicted Height Calculated (Altitude) and Azimuth (True Bearing) of 3 Celestial Bodies on 26 May 2021 at 23:59Z.
Using a MOBOARD, plot our AP as being at the center of the Board.
AP
As a scale, each circle is equivalent to 300nm.
300nm
600nm
900nm
1200nm
2400nm
1800nm
1500nm
2100nm
2700nm
3000nm
Pollux – HC = 42° / Azimuth 275°(T)
Distance of the GP from the AP =
90-42 = 48° x 60nm
= 2880nm
Kochab – HC = 48° / Azimuth 018°(T)
Distance of the GP from the AP =
90-48 = 42° x 60nm
= 2520nm
Denebola – HC = 65° / Azimuth 171°(T)
Distance of the GP from the AP =
90-65 = 25° x 60nm
= 1500nm
Now plot the position of Celestial Bodies Geographic Positions, in relation to us, based on their Height Calculated and Azimuth.

## Slide 24
Using the Stars
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-When we have identified the preferred CBs to calculate our position, we will observe their actual Altitudes using a sextant.
-We take a minimum of 3 sights. Try to always take more if possible!
-The Altitude is the angle between the visible horizon and the CB. It will be a value between 0°-90°.
-We will then have the sights needed to calculate a fix.

## Slide 25
Using the Stars
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Rather than use the entire LOP circle, which can be enormous, we will only use a portion of it.
-What begins as a circle, is then viewed as a straight line that can be plotted onto a chart.
-How is this accomplished?

## Slide 26
Altitude Intercept Method
The Altitude Intercept Method again compares the Height Calculated, from STELLA or Pub 249, against the Height Observed.
AP
30°
HC
Azimuth - 085
The Azimuth (True Bearing) of the Celestial Body from the AP is predicted at 085°(T).
GP
The HC is 30° which equals a distance 3600nm between the GP and AP.
HC distance calculation =
90°-30° = 60°x 60nm =
3600nm
But instead of relating the distances to the Geographic Position of a Celestial Body, it based entirely upon the Assumed Position.

## Slide 27
Altitude Intercept Method
AP
30°
HC
Azimuth - 085
We take a Sight of the Celestial Body using a Sextant, correcting for Index Error, Height of Eye, Barometric Pressure and Temperature to get Height Observed (HO).
The HO will be larger or smaller than the HC because our DR is very unlikely to be 100% accurate.
HO distance = 3660nm
In this case, the Altitude or HO is 29.5° which is less than the HC by 0.5°.
GP
29.5°
HC distance = 3600nm
More easily, if 1° = 60nm then 0.5° difference between HC and HO = 30nm.
If the HO is less than the HC, in terms of distance, we must be further away from the Geographic Position (GP) on a bearing opposite to the Azimuth.
If HO is more than HC, we must be closer to the Geographic Position (GP) along the Azimuth.
HO distance calculation = 90°-29.5° = 30.5°x 60nm =
3630nm
HO

## Slide 28
Altitude Intercept Method
AP
Azimuth - 085
Right now however, we still have a circle.
We want to represent the circle as a straight line to make a usable LOP.
To do this, we draw a line perpendicular to the Azimuth of the Celestial Body from AP, at the new position.
GP
LOP
Because HO was less than HC, this line is drawn on true bearing opposite to the Azimuth.
HO<HC therefore opposite to Azimuth - 265°(T) from AP.
Perpendicular – line is drawn at 90° to Azimuth – therefore 355 to 175°
We now have a single line of position. Just as with a Circle of Equal Altitude, all we know is that we are somewhere on this line. We need 2 more lines to intersect for a 3 point fix.

## Slide 29
Altitude Intercept Method
AP
GP
GP
GP
Hc = 66°
Ho = 66°30’
= 30NM toward GP
Hc = 70°
Ho = 69° 45’
= 15NMs away from GP
Hc = 44°
Ho = 45°
= 60 NMs toward GP
Azimuth
Azimuth
Azimuth
Hc
Hc
Hc
Ho
Ho
Ho
30nm
15nm

## Slide 30
Plot our AP as being at the center of the Board.
AP
As a scale, each circle is equivalent to 6nm.
6nm
12nm
18nm
24nm
48nm
36nm
30nm
42nm
54nm
60nm
Pollux – HC = 42° Azimuth 275°(T)
HO 42.15°
Kochab – HC = 27° / Azimuth 048°(T)
HO = 27.05°
Denebola
HC = 65°
Azimuth 171°(T)
HO = 64.8°
How far is our Fix from the Assumed Position?
Approximately 13nm. Not a bad update if the Ship hadn’t been able to fix in a few days!
Difference = 9nm
Toward as HO > HC

## Slide 31
Altitude Intercept Method
NN310 Advanced Navigation
SEANAV I U.S. Naval Academy I Celestial Navigation
Before STELLA, a Celestial Fix would be plotted on a Plotting Form manually using the Altitude Intercept Method.
Now, provided we input the right information, the system will plot and generate a Fix position for us to then update our Navigational Plot on ECDIS or a paper chart.

## Slide 32
CELNAV During the Day
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Using the stars, we can get a 3 point Celestial Fix twice a day, during the Twilight before Sunrise and the Twilight after Sunset.
-CELNAV doesn’t stop there.
-There are ways to calibrate equipment and fix a position during the day using CELNAV.

## Slide 33
Gyro Compass Error
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-During the planning phase of CELNAV, we found the time of Sunrise and Sunset.
-Typically, we will also find the bearing of Sunrise and Sunset as well.
-The Sun rises in the East and sets in the West, but due to the effects of our Latitude and the Declination of the Sun, the exact bearing will change by a small amount.
-If we know the bearing of Sunrise or Sunset, we can take a bearing of it with our Gyro Compass and determine if an error exists.

## Slide 34
Sunrise and Sunset
So when exactly is Sunrise and Sunset?
When the sun’s light hits the atmosphere, the change in density causes the path of light to change.
The is therefore the Perceived Position of the Sun; where we see it.
Then there is the True Position of the Sun; where it is due to refraction.
True Sunrise or Sunset is when the Sun is at 34 minutes of Arc (Altitude) above the Visible Horizon. That is 0.56°
This position can also be described as a ‘Semi Diameter’ above the Horizon.
At Sunrise or Sunset, the Sun’s Apparent position is 34’ minutes (0.56° Altitude) or a ‘Semi Diameter’ above the Horizon.
Sun’s True Position at SR/SS is not visible above the horizon due to refraction.
When the Sun is 12° below the Visible Horizon, it is the Start or End of Nautical Twilight.
12°
When the Sun is 6° below the Visible Horizon, it is the Start or End of Civil Twilight.
6°

## Slide 35
Sunrise and Sunset
To use Sunrise / Sunset we have to be able to calculate the time.
Time of Sunrise / Set
  Listed in the Nautical Almanac
  Tabulated for Latitude
  Our DR Position is 40°N 76°W
  Sunset time 40°N = 1904Z
    Interpolate for
      Own latitude
      The correct day
  Adjust for your longitude (Arc to Time)
  Long = 76° W = 5Hr 04Min
  West is Best so add to Sunset = 0008Z
  Adjust for Time Zone +5R therefore subtract 5hrs = 1908R
  Same process to predict Twilight/Moonrise/Moonset)

## Slide 36
Bearing of Sunrise and Sunset
Once we have calculated the Time of SR / SS, we can calculate the bearing.
So why is this important? Especially when we don’t have GPS available, navigation and our weapon and sensor systems are reliant on accurate Gyro Compass inputs.
In aviation terms, 1° of heading error at 60nm will result in 1nm of error at destination.
1° Heading Error will result in a 1nm track error at 60nm
1nm
For Ships, using a navigation mark as a head bearing, 1° of error at 1nm is 35yds or 100ft. This can be used in navigation terms to assess track visually.
Our charted Head Bearing should be 032°. If it bears 033° we are left of track. 031° and we are right of track.
1° = 35yds at 1nm.
Bears 033° @ 2nm
2 x 35 = 70yds per degree

## Slide 37
Bearing of Sunrise and Sunset
A more worrying example:
  Our weapon systems find direction from the Ship’s gyro when no GPS input is available.
  An Gyro error will impact weapon direction and targeting.
  Loss of gyro means we can’t use our weapons in many cases.
Enemy Position
SF Advanced Forces – “Call for Fire”
DDG is providing Naval Fires support 6 miles off the coast.
‘Call For Fire – Danger Close’ received against Enemy Position at 10nm from the Ship.
Ship has an unknown 2° East gyro error.
2° at 10nm = 700yds or 2000ft error placing friendly troops at risk!

## Slide 38
Bearing of Sunrise and Sunset
Bearing of Sunrise / Set
  Sun’s Declination listed in the Nautical Almanac
  Used to predict bearing of sun at SR/SS
    Determine declination of Sun in GMT (UT)
    Combine Declination and Latitude to ‘True Amplitude’
      Angular distance from 090 or 270
      Mathematically - TA - (Inv)Sin = Sin (Dec) / Cos (Lat)
    Add/Subtract TA to get true bearing of SR/SS

## Slide 39
Bearing of Sunrise / Set
  E.g. Ship’s position 40°20’N 076°30’W
  Time of Sunset 1908R (0008Z)
  Declination of Sun N17° 31’.0
  True Amplitude (North Dec > Add) Approx 23°
  Bearing of Sun at SS 270 + 23°
  = 293° (T)
  Gyro at Sunset 292°
  Gyro Error 1° East
  *TA - (Inv)Sin = Sin (Dec) / Cos (Lat)
  Don’t worry – STELLA has replaced the book!
Bearing of Sunrise and Sunset

## Slide 40
Bearing of Sunrise and Sunset
Bearing of Sunrise / Set
  Bearing of Sun Set 293° (T)
  Gyro at Sunset 292° (PGC)
  Gyro Error 1°E
Bearing taken by Gyro 292
Error = 1°E – we add 1° to any visual bearings or to weapon systems.

## Slide 41
Video: Gyro Error with an Azimuth Circle
https://www.youtube.com/watch?v=NsGVSC94ztw

## Slide 42
CELNAV During the Day
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-After Sunrise when we conduct our first Gyro Compass error check, we can still conduct CELNAV.
-We can use the Sun to generate LOPs throughout the day.
-What kind of fix uses one NAVAID over a period of time to generate 3 LOPs?

## Slide 43
Using the Sun
The Altitude of the Sun changes throughout the day.
Using math, 90°-ALT=COALT we can calculate our distance from the Sun’s GP during the day giving us an LOP.
We need 3 LOPs to get a good fix. However, the rate of movement of the Sun means that we need to leave time between each Sight in order to allow there to be a visible change.
By taking 3 Sights at different times during the day, we can take a Running Fix from the Sun provided that we take into account the Time, Course and Speed of the Ship.
DR
New DR
Transferred Position Line from Morning
Second Sight normally taken at Noon.
LOP based on our first position line in the Morning
New DR
Third Sight normally taken during the Afternoon.
Transferred Position Lines
Running Fix based on DR

## Slide 44
Sun – Run – Sun
1000Z
1206Z
1500Z
Sun’s Geographic Position (GP).
Sun Rises in The East and Sets in the West.
The GP moves westerly with the Sun due to the Earth’ rotation.
Using a Running Fix and applying the principles of the Altitude Intercept Method, we can gain a fix during the day but just using the Sun.

## Slide 45
Sun – Run – Sun
Using a Running Fix and applying the principles of the Altitude Intercept Method, we can gain a fix during the day but just using the Sun.
90º - Alt = Co-Alt
37º 38.6’
The Height Observed at 1000Z = 52º 21.4’
What is the Co-Alt?
What is the distance?
Co-Alt x 60nm = 2258.6 NM
Sun Sight taken during the Morning

## Slide 46
Sun – Run – Sun
Using a Running Fix and applying the principles of the Altitude Intercept Method, we can gain a fix during the day but just using the Sun.
The Height Observed at 1206Z = 62º 37.7’
What is the Co-Alt?
What is the distance?
Sun Sight taken at Noon
Co-Alt 27º 22.3’
1642.3 NM
Lat 50º 49.1’

## Slide 47
Sun – Run – Sun
Using a Running Fix and applying the principles of the Altitude Intercept Method, we can gain a fix during the day but just using the Sun.
Co-Alt 43º 09.5’
The Height Observed at 1500Z = 46º 50.5’
What is the Co-Alt?
What is the distance?
2589.5 NM

## Slide 48
CELNAV During the Day
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-While using the Sun-Run-Sun method to determine our position, we take three sights of the Sun throughout the day.
-The 2nd Sun LOP has some additional significance, as it is taken during Local Apparent Noon (LAN), or when the Sun crosses our Meridian.

## Slide 49
Meridian Passage / Local Noon
50º 00’N
50º 30’N
49º 30’N
008º W
009º W
010º W
011º W
1238
1242
1246
1250
Mer Pass 1248
The time of MERPASS varies based on the Sun’s Declination and our Longitude.
The Nautical Almanac lists the time of MERPASS at Greenwich.
DR Longitude
The Time of MERPASS changes by 4 mins every 1° of Longitude.

## Slide 50
Meridian Passage / Local Noon
By taking a Sight at Meridian Passage, we can gain not only our distance from the Sun’s GP but we can also calculate our Latitude.
Zenith
Equator
E
W
N
S
Observer’s
Meridian
Altitude
Latitude
Declination (from N.A.)
Pole
Co-altitude
Observer’s Horizon
By calculating our Co-Alt from the Sight, and then adding or subtracting the Sun’s Declination, we can calculate Latitude.

## Slide 51
Meridian Passage / Local Noon
Zenith
Pole
Equator
True Altitude
Dec N20 °
Co-Alt
When Latitude and Declination are in same hemisphere and Lat is > Dec
Latitude = Declination + Co-Altitude
Latitude 40°N
Observer’s Horizon

## Slide 52
Meridian Passage / Local Noon
52
Zenith
Pole
Equator
True Altitude
Dec
Co-Alt
When Latitude and Declination are in opposite hemispheres
Latitude
Observer’s Horizon
Latitude = Co-Altitude - Declination

## Slide 53
Day’s Work in Celestial Navigation
Now that we have explored the different ways in which to Fix the Ship’s Position to prove equipment correct, how do we execute this on a transit across the Atlantic?
CELNAV is a Team game – Each Watch needs to have the basic knowledge to be able to execute the CELNAV task that relates to their Watch.
Morning Stars
Taken between Nautical Twilight and Sun Rise
3 Point Fix by LOP
Sunrise
Morning
Local Noon
Afternoon
Sunset
Evening Stars
Taken between Sunset and Nautical Twilight
34’ of Arc / Sun Semi Diameter above horizon
Gyro Check
Gyro Check
34’ of Arc / Sun Semi-Diameter above horizon
Take Sight of Sun’s Altitude
Gain 1 LOP
Second LOP and Latitude
Take Sight of Sun’s Altitude
Take Sight of Sun’s Altitude
3 Point Fix by LOP
Third LOP – complete running fix

## Slide 54
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 – DESCRIBE The planning involved to conduct CELNAV. 2 - DEFINE Local Hour Angle in relation to identifying Celestial Bodies (CBs). 3 - DESCRIBE Dead Reckoning and relationship of Assumed Position (AP) to Time. 4 - EXPLAIN How to identify the best CBs to navigate from. 5 - EXPLAIN Circle of Equal Altitude. 6 - DESCRIBE The Altitude Intercept Method. 7 - DEFINE Sunrise / Sunset in relation to the Visible Horizon. 8 - DESCRIBE The importance of accurate Gyro Compasses and effect on Navigation / Weapon Systems. 9 - EXPLAIN How to calculate Gyro Error from the bearing of Sunrise / Sunset. 10 - DESCRIBE How to fix from the Sun using a Running Fix (Sun Run Sun). 11 - DESCRIBE Meridian Passage and the calculation of Latitude. 12 - DESCRIBE The Day’s Work in Celestial Navigation.

## Slide 55
Questions?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy